## Slide 1: Segmentation for Robotic Arm
Snir Green and Ethan Baron

## Slide 2: Problem Definition
- Part of Robotics Excellence Program in mechanical engineering department
- Building a robotic arm that picks cans from a clutter in a box and organizes it for shipment
- The robotic arm will use vacuum or other measures to lift a can.
Notes: TODO: Snir should take a photo of the robot arm

## Slide 3: Problem Definition – For us
- A depth camera (LIDAR) is located above the crate in a fixed position.
- Our task – Get a picture (RGBD) and return the location/curve of the most upper can.

## Slide 4: The Algorithm – High Level

## Slide 7: The Algorithm - Manager
Take picture
RGBD image
RGBD image
masks
proccessing

## Slide 9: The Algorithm – Mask R-CNN
- CNN
- SOTA in image segmentation and instance segmentation
- Based on Faster R-CNN which is a region-based CNN
Notes: - It gives bounding boxes as well, we don’t use it.

## Slide 10: The Algorithm – Mask R-CNN
- We used the PyTorch version, and the checkpoint trained on the COCO dataset.
- Contains 88 classes, none are cans

## Slide 11: The Algorithm – Mask R-CNN
- Without training, the checkpoint performed OK and identified the cans as bottles.
Notes: Should remind here we only need one can right
In the simpler scenarios – it worked quite well, (with identifying one can, in the harder it was BAD).
Explain that thus with a request from the robotics lab and Amit guidance, we trained the network

## Slide 12: Data gathering
Taking pictures of 1200 scenarios.
Creating the masks of the cans.
Classifying laying, standing and tilted cans.

## Slide 13: The Algorithm – Mask R-CNN
- It did perform more than 90% on our tests in medium difficult environment (performed afterwards).
Notes: Should remind here we only need one can right
In the simpler scenarios – it worked quite well, (with identifying one can, in the harder it was BAD).

## Slide 14: The Algorithm – Mask R-CNN
Some error examples though:
Notes: TODO: M

## Slide 15: The Algorithm – Mask R-CNN
Some error examples though:

## Slide 17: The Algorithm – 3D Most Upper Mask
- Using the depth matrix (Z dimension)
- Calculates for every mask the maximal height in it
- Takes highest mask
Notes: - Remember this is after smoothing the masks only
- Sometimes fail (probably due to not doing some percentiles in the code…) but only to similar heighted cans

## Slide 19: Before That – Quick Detour on the Depth Camera
Notes: - Remember this is after smoothing the masks only
Sometimes fail (probably due to not doing some percentiles in the code…) but only to similar heighted cans
Remind why we don’t do it with Hough Transform

## Slide 20: Depth Camera Noise ADD HERE
Notes: - First of all show differences in heights in the camera

## Slide 21: Depth Camera Noise – Comparison
84mm
106mm
130mm
128mm
134mm
129mm
Notes: Left side – laying can, right side – standing can, in the middle of the frame

## Slide 22: Depth Camera Noise – Comparison
82mm
104mm
104mm
129mm
117mm
114mm
91mm
Notes: This is after another gaussian filter on the mask () and uniform filter sized 40x40.
As you can see, the differences only grew (on the edges) bigger because of the huge size of the uniform kernel
We tried to study something based on the difference between percentiles in height the different scenarios
Tried various methods of smoothing : Gauss, Median, Uniform
Ended up with that method and separated by empirical separation of the cases, without cans on the side which we excluded with too much noise.
This is after another gaussian filter on the mask (𝜎=2) and uniform filter sized 40x40.
As you can see, the differences only grew (on the edges) bigger because of the huge size of the uniform kernel
We tried to study something based on the difference between percentiles in height the different scenarios
Tried various methods of smoothing : Gauss, Median, Uniform
Ended up with that method and separated by empirical separation of the cases, without cans on the side which we excluded with too much noise.

## Slide 23: Depth Camera Noise – 1st Derivative
Notes: This is after another gaussian filter on the mask () and uniform filter sized 40x40.
Tried to do summing or avg over the derivative matrix
Didn’t find something that always succeeds in separating by first derivative.
This is after another gaussian filter on the mask (𝜎=2) and uniform filter sized 40x40.
Tried to do summing or avg over the derivative matrix
Didn’t find something that always succeeds in separating by first derivative.

## Slide 24: Depth Camera Noise – 1st Derivative
82mm
298e-5
23.6e-5
162e-5
12.4e-5
282e-5
132e-5
Notes: This is after another gaussian filter on the mask () and uniform filter sized 40x40.
Tried to sum over all the derivatives abs, mostly worked well but again in cans on the side made too much noise..
There is an idea that the shape becomes quite distinct – we didn’t go into that.
This is after another gaussian filter on the mask (𝜎=2) and uniform filter sized 40x40.
Tried to sum over all the derivatives abs, mostly worked well but again in cans on the side made too much noise..
There is an idea that the shape becomes quite distinct – we didn’t go into that.

## Slide 25: Depth Camera Noise – 2nd Derivative
Notes: This is after another gaussian filter on the mask ()
This is after another gaussian filter on the mask (𝜎=2)

## Slide 26: Depth Camera Noise – 2nd Derivative
Notes: This is after another gaussian filter on the mask () and uniform filter sized 40x40.
Looks better – but again, we didn’t find any absolute measure to distinct between those.
This is after another gaussian filter on the mask (𝜎=2) and uniform filter sized 40x40.
Looks better – but again, we didn’t find any absolute measure to distinct between those.

## Slide 27
Notes: Quick Reminder of what we are trying to do here!!!

## Slide 28: What we actually did
- By empirical means, we found that mostly for standing cans
- the distance .
- Important to note that this condition does not hold in the far-right end of the camera.
Notes: again, everything with noise is quite empirical.
Important to note we checked that the camera’s setup is good – (but maybe that was one of the problems?)

## Slide 29
Notes: Quick Reminder of what we are trying to do here!!!
Add that if we find that the most upper can is standing thus we go here

## Slide 31: Bits algorithm
Get the masks of the standing cans
Proccess a masked image
Find canny image
Finding small circles

## Slide 32: Bits algorithm – heuristics
Running Hough Transform with different parameters
Finding the best fit using heuristics:
  Distance from center.
  Occurrences.
  Distance from mean point.
  Etc.

## Slide 33: Bits algorithm – find ”sweet spot”

## Slide 35: The Algorithm – Rectangle Around Mask
- We draw a rotated rectangle around if not standing can
- Performing PCA on the points to get the rectangle.
Notes: Mostly for noise cancelation (sometimes the mask is not quite smooth as we want, and from above all the cans are somewhat rectanglic).

## Slide 37: The Algorithm – Axis split
- Checks if can is laying along the main curve
- Splits based on the top point
- Checks the second derivatives along turquoise lines
Notes: We do here gauss filter as well with .
We do here gauss filter as well with 𝜎=1.

## Slide 39: The Algorithm – Pix2cm
Pix2cm ratio is linear in the distance from floor.
Measure distance from floor.
Using percentile in the area of the point to remove camera noise.

## Slide 41: Results

## Slide 42: Experiment setup
A cardbox painted white.
Camera is located ~60 cm above the “ground”.
Different scenarios:
  Standing cans.
  Laying cans.
  Tilted cans.
  Clutter.

## Slide 43: Results
Chart: 
| Results
Success | 29
Wrong Side | 8
Mask Failure | 2
~73%
~20%
~7%

## Slide 44: Results - success

## Slide 45: Results – wrong side

## Slide 46: Results – mask failure

## Slide 49: Suggested Improvements
- Less noisy camera / not based on LIDAR
- Working on reducing camera noise with algorithmic approach
- Training the Mask R-CNN on more data and more various data
- Converting the whole program into custom NN with tailor made loss function